推荐认可的实验室检测能力范围（中文）

名称：洛阳LYC轴承有限公司检测试验中心

地址：洛阳市涧西区建设路96号

| 序号 | 检测对象 | 项目/参数 | 领域代码 | 检测标准（方法）名称及编号（含年号） | 说明 | 备注 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | 序号 | 名称 |  |  |  |  |
| 1 | 滚动轴承(参数) | 1 | 尺寸公差和旋转精度 | 030704 | 滚动轴承 测量和检验的原则及方法 GB/T 307.2-2005 7,8,9,10,11,12，13,14,15 | 只测：12mm≤d≤1000mm，30mm≤D≤1400mm |  |
|  |  |  |  |  | 滚动轴承 向心轴承 公差 GB/T 307.1-2005 5.1,5.2,5.3,5.4 |  |  |
|  |  |  |  |  | 滚动轴承第4部分:推力轴承公差 GB/T 307.4-2012 5.2,5.3,5.4,5.5 |  |  |
|  |  |  |  |  | 滚动轴承及其零件 补充技术条件 JB/T 10336-2002 4.1.1.3,4.1.1.4,4.2.1.2,4.2.1.4,4.2.1.5,4.2.1.5,4.2.1.7 |  |  |
|  |  | 2 | 游隙 | 030704 | 滚动轴承 径向游隙的测量方法 GB/T 25769-2010 6,7,8,9 | 只测:32mm≤D≤1000mm |  |
|  |  |  |  |  | 滚动轴承 双列和四列圆锥滚子轴承 游隙及调整方法 JB/T 8236-2010 4,5 |  |  |
|  |  |  |  |  | 滚动轴承 外球面球轴承 径向游隙 GB/T 25766-2010 6.1,7 |  |  |
|  |  |  |  |  | 滚动轴承 游隙 第1部分：向心轴承的径向游隙 GB/T 4604.1-2012 5 |  |  |
|  |  |  |  |  | 滚动轴承 游隙 第2部分： 四点接触球轴承的轴向游隙 GB/T4604.2 -2013 5 |  |  |
|  |  | 3 | 残磁 | 030704 | 滚动轴承 残磁及其评定方法 JB/T 6641-2007 5 | 只测:≤10mT |  |
|  |  | 4 | 清洁度 | 030704 | 滚动轴承 清洁度评定方法 JB/T 7050-2005 7 | 只测:杂质≤200mg |  |
|  |  | 5 | 振动 | 030704 | 滚动轴承 振动测量方法 第1部分：基础 GB/T 24610.1-2009 6 | 只测：30mm≤D≤200mm |  |
|  |  |  |  |  | 滚动轴承 振动测量方法 第2部分：具有圆柱孔和圆柱外表面的向心球轴承 GB/T 24610.2-2009 5 |  |  |
|  |  |  |  |  | 滚动轴承 振动测量方法 第3部分：具有圆柱孔和圆柱外表面的调心滚子轴承和圆锥滚子轴承 GB/T 24610.3-2009 5 |  |  |
|  |  |  |  |  | 滚动轴承 振动测量方法 第4部分：具有圆柱孔和圆柱外表面的圆柱滚子轴承 GB/T 24610.4-2009 5 |  |  |
|  |  |  |  |  | 滚动轴承深沟球轴承振动（速度）技术条件 GB/T 32325-2015 6 |  |  |
|  |  |  |  |  | 滚动轴承 圆柱滚子轴承振动（速度）技术条件 JB/T8922-2011 4 |  |  |
|  |  |  |  |  | 滚动轴承圆锥滚子轴承振动（速度）技术条件 JB/T10236-2014 6 |  |  |
|  |  |  |  |  | 滚动轴承 圆锥滚子轴承 振动(加速度)技术条件 JB/T 10237-2014 6 |  |  |
|  |  |  |  |  | 滚动轴承 振动(加速度)测量方法及技术条件 GB/T 32333-2015 6 |  |  |
|  |  | 6 | 外观 | 030704 | 滚动轴承 产品标志 GB/T 24605-2009 7 |  |  |
|  |  |  |  |  | 滚动轴承 防锈包装 GB/T 8597-2013 4.2.4,4.1,4.3.2,4.3.3,4.4 |  |  |
|  |  |  |  |  | 滚动轴承及其零件补充技术条件 JB/T10336-2002 4.1.1.5,4.1.1.6,4.1.1.7,4.1.1.8,4.1.1.9,4.1.1.10,4.1.1.11,4.1.2.1,4.1.2.2,4.2.2.1,4.2.2.2 |  |  |
|  |  |  |  |  | 滚动轴承零件 套圈和滚子外观质量要求 CSBTS TC98.54-1999 4,5,6 |  |  |
|  |  | 7 | 寿命试验 | 030704 | 滚动轴承 寿命与可靠性试验及评定 GB/T 24607-2009 |  |  |
|  |  |  |  |  | 机车车辆轴箱滚动轴承在试验机上的耐久试验 TB/T 3017-2001 | 只测：100mm≤d≤180mm |  |
| 2 | 转盘轴承 | 1 | *尺寸公差 | 030704 | 滚动轴承转盘轴承 JB/T10471-2004 6.5.1 | 只测：200mm≤D≤6300mm；不测：齿轮参数 |  |
|  |  | 2 | *旋转精度 | 030704 | 滚动轴承转盘轴承 JB/T10471-2004 6.5.2,7.1 | 只测： 200mm≤D≤6300mm |  |
|  |  | 3 | *游隙 | 030704 | 滚动轴承转盘轴承 JB/T10471-2004 6.8,7.3 | 只测：200mm≤D≤6300mm |  |
| 3 | 风力发电机组偏航,变桨轴承 | 1 | *尺寸公差 | 030704 | 滚动轴承风力发电机组偏航,变桨轴承 GB/T29717-2013 7.3.1 | 只测：200mm≤D≤6300mm；不测：齿轮参数 |  |
|  |  | 2 | *旋转精度 | 030704 | 滚动轴承风力发电机组偏航,变桨轴承 GB/T29717-2013 7.3.2 | 只测：200mm≤D≤6300mm |  |
|  |  | 3 | *游隙 | 030704 | 滚动轴承风力发电机组偏航,变桨轴承 GB/T29717-2013 7.5 | 只测：200mm≤D≤6300mm |  |
| 4 | 鼓风机轴承 | 1 | 尺寸公差 | 030704 | 滚动轴承 鼓风机轴承 技术条件 JB/T 7753-2007 3.2,4.1 |  |  |
|  |  | 2 | 旋转精度 | 030704 | 滚动轴承 鼓风机轴承 技术条件 JB/T 7753-2007 3.2,4.1 |  |  |
| 5 | 滚针和双向推力圆柱滚子组合轴承 | 1 | 尺寸公差 | 030704 | 滚动轴承 滚针和双向推力圆柱滚子组合轴承 GB/T 25768-2010 7.2 |  |  |
|  |  | 2 | 旋转精度 | 030704 | 滚动轴承 滚针和双向推力圆柱滚子组合轴承 GB/T 25768-2010 7.2 |  |  |
| 6 | 机床轴承 | 1 | 尺寸公差 | 030704 | 滚动轴承 机床丝杠用推力角接触球轴承 GB/T 24604-2009 7.2 |  |  |
|  |  |  |  |  | 滚动轴承机床主轴用双向推力角接触球轴承 JB/T6362-2007 7,8.1,8.2 |  |  |
|  |  |  |  |  | 滚动轴承 机床主轴用圆柱滚子轴承 GB/T 27559-2011 7.2,8.1 |  |  |
|  |  | 2 | 旋转精度 | 030704 | 滚动轴承机床主轴用双向推力角接触球轴承 JB/T6362-2007 7 |  |  |
|  |  |  |  |  | 滚动轴承 机床主轴用圆柱滚子轴承 GB/T 27559-2011 7.2,8.1 |  |  |
|  |  | 3 | 游隙 | 030704 | 滚动轴承 机床主轴用圆柱滚子轴承 GB/T 27559-2011 7.5,8.3 |  |  |
| 7 | 机器人用薄壁密封轴承 | 1 | 尺寸公差 | 030704 | 滚动轴承 机器人用薄壁密封轴承 JB/T 6636-2007 6.1,7.1 |  |  |
|  |  | 2 | 游隙 | 030704 | 滚动轴承 机器人用薄壁密封轴承 JB/T 6636-2007 6.5 |  |  |
| 8 | 汽车发电机轴承 | 1 | 尺寸公差 | 030704 | 滚动轴承 汽车发电机轴承 技术条件 JB/T 8167-2006 2 |  |  |
|  |  | 2 | 旋转精度 | 030704 | 滚动轴承 汽车发电机轴承 技术条件 JB/T 8167-2006 2 |  |  |
|  |  | 3 | 游隙 | 030704 | 滚动轴承 汽车发电机轴承 技术条件 JB/T 8167-2006 3.6 |  |  |
|  |  | 4 | 振动 | 030704 | 滚动轴承 汽车发电机轴承 技术条件 JB/T 8167-2006 3.7 |  |  |
| 9 | 汽车轮毂轴承单元 | 1 | 游隙 | 030704 | 滚动轴承汽车轮毂轴承单元 JB/T 10238-2011 9.4 |  |  |
| 10 | 深沟球轴承 | 1 | 游隙 | 030704 | 滚动轴承电机用深沟球轴承 技术条件 GB/T 28698-2012 5.6,6.3 |  |  |
|  |  | 2 | 填脂量 | 030704 | 滚动轴承密封深沟球轴承技术条件 JB/T 7752-2005 4.5 | 只测:≤200g |  |
| 11 | 推力轴承 | 1 | 尺寸公差 | 030704 | 滚动轴承 推力调心滚子轴承 技术条件 JB/T 7750-2007 4.2,5.1 |  |  |
|  |  |  |  |  | 滚动轴承 推力圆柱滚子和保持架组件及推力垫圈 JB/T 8211-2005 6.2,7.1 |  |  |
|  |  |  |  |  | 滚动轴承 推力圆锥滚子轴承 JB/T 7751-2016 7.2,8.1 |  |  |
| 12 | 组配角接触球轴承 | 1 | 尺寸公差 | 030704 | 滚动轴承 组配角接触球轴承 技术条件 JB/T 10186-2010 6.1.4,附录A |  |  |
|  |  | 2 | 旋转精度 | 030704 | 滚动轴承 组配角接触球轴承 技术条件 JB/T 10186-2010 6.1.3, 附录A |  |  |
| 13 | 精品轴承 | 1 | 尺寸公差 | 030704 | 精品轴承 技术条件 CSBTS TC98.76-2001 2,7.1 |  |  |
|  |  | 2 | 旋转精度 | 030704 | 精品轴承 技术条件 CSBTS TC98.76-2001 2 |  |  |
|  |  | 3 | 游隙 | 030704 | 精品轴承 技术条件 CSBTS TC98.76-2001 6.5 |  |  |
|  |  | 4 | 振动 | 030704 | 精品轴承 技术条件 CSBTS TC98.76-2001 6.6.1,6.6.3 |  |  |
| 14 | 铁路轴承 | 1 | 尺寸公差 | 030704 | 铁道车辆滚动轴承 TB/T2235-2010 2,5.6 |  |  |
|  |  |  |  |  | 滚动轴承 铁路客车轴承 GB/T25772-2010 8.2,9.2 |  |  |
|  |  |  |  |  | 滚动轴承 铁路机车轴承 GB/T25771-2010 9.2,10.2 |  |  |
|  |  |  |  |  | 滚动轴承 铁路货车轴承 GB/T25770-2010 8.2,9.2 |  |  |
|  |  | 2 | 旋转精度 | 030704 | 铁道车辆滚动轴承 TB/T2235-2010 2,5.6 |  |  |
|  |  |  |  |  | 滚动轴承 铁路客车轴承 GB/T25772-2010 8.2,9.2 |  |  |
|  |  |  |  |  | 滚动轴承 铁路机车轴承 GB/T25771-2010 9.2,10.2 |  |  |
|  |  |  |  |  | 滚动轴承 铁路货车轴承 GB/T25770-2010 8.2,9.2 |  |  |
|  |  | 3 | 游隙 | 030704 | 铁道车辆滚动轴承 TB/T2235-2010 4.2.1 |  |  |
|  |  |  |  |  | 滚动轴承 铁路客车轴承 GB/T25772-2010 8.3,9.3 |  |  |
|  |  |  |  |  | 滚动轴承 铁路机车轴承 GB/T25771-2010 9.3,10.3 |  |  |
| 15 | 凸缘外圈向心球轴承 | 1 | 尺寸公差 | 030704 | 滚动轴承凸缘外圈向心球轴承凸缘尺寸 GB/T7217-2013 5 |  |  |
| 16 | 圆柱滚子轴承 | 1 | 尺寸公差 | 030704 | 滚动轴承 双列满装圆柱滚子滚轮轴承 JB/T 7754-2007 8.2,9.1 |  |  |
| 17 | 轧机轴承 | 1 | 尺寸公差 | 030704 | 滚动轴承 轧机用双列和四列圆锥滚子轴承 JB/T 5389.2-2005 6.1,7.1 |  |  |
|  |  |  |  |  | 滚动轴承 轧机用滚子轴承第1部分:四列圆柱滚子轴承 JB/T 5389.1-2016 7.2,8.1 |  |  |
|  |  |  |  |  | 滚动轴承 轧机压下机构用满装圆锥滚子推力轴承 JB/T 3632-2015 8.2,9.1 |  |  |
|  |  | 2 | 旋转精度 | 030704 | 滚动轴承 轧机用双列和四列圆锥滚子轴承 JB/T 5389.2-2005 6.1 |  |  |
|  |  |  |  |  | 滚动轴承 轧机用滚子轴承第1部分:四列圆柱滚子轴承 JB/T 5389.1-2016 7.2 |  |  |
|  |  | 3 | 游隙 | 030704 | 滚动轴承 轧机用双列和四列圆锥滚子轴承 JB/T 5389.2-2006 7.2 |  |  |
|  |  | 4 | 残磁 | 030704 | 滚动轴承 轧机压下机构用满装圆锥滚子推力轴承 JB/T 3632-2015 8.4,9.5 | 只测：≤10mT |  |
| 18 | 滚动轴承零件（参数） | 1 | 圆度 | 030704 | 滚动轴承零件 圆度和波纹度误差测量及评定方法 GB/T 32324-2015 4.1.3,6.1.1 | 只测：D≤400mm |  |
|  |  |  |  |  | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.3 |  |  |
|  |  | 2 | 粗糙度 | 030704 | 滚动轴承零件 表面粗糙度测量和评定方法 JB/T 7051-2006 5.1,5.2,5.3,5.4,6.1 | 只测：D≤400mm |  |
| 19 | 钢球 | 1 | 尺寸公差 | 030704 | 滚动轴承 球 第1部分： 钢球 GB/T 308.1-2013 6.5,7.1 | 只测:6mm≤Dw≤53mm |  |
|  |  | 2 | 球形误差 | 030704 | 滚动轴承 球 第1部分： 钢球 GB/T 308.1-2013 6.4,7.2 | 只测:6mm≤Dw≤53mm |  |
|  |  | 3 | 外观 | 030704 | 滚动轴承钢球表面缺陷及评定方法 JB/T10861-2008 4 |  |  |
|  |  | 4 | 钢球振动 | 030704 | 滚动轴承 钢球振动(加速度)技术条件 JB/T 8923-2010 5,6 | 只测:5mm≤Dw≤30mm |  |
| 20 | 圆柱滚子 | 1 | 尺寸公差 | 030704 | 滚动轴承 圆柱滚子 GB/T 4661-2015 6.3,7.1,7.3,7.5 | 只测:10mm≤Dw≤53mm |  |
|  |  | 2 | 形位公差 | 030704 | 滚动轴承 圆柱滚子 GB/T 4661-2015 6.3,7.2,7.4 |  |  |
| 21 | 圆锥滚子 | 1 | 尺寸公差 | 030704 | 滚动轴承 圆锥滚子 GB/T 25767-2010 6.2.2,7.1.1,7.1.2 | 只测:6mm≤Dw≤70mm |  |
|  |  | 2 | 形位公差 | 030704 | 滚动轴承 圆锥滚子 GB/T 25767-2010 6.2.2,7.1.3,7.1.4,7.1.5,7.3.1, |  |  |
| 22 | 球面滚子 | 1 | 尺寸公差 | 030704 | 滚动轴承零件 球面滚子技术条件 CSBTS TC98.69-1999 6.2.1,6.2.2,6.2.3,5.1,5.2 | 只测:10mm≤Dw≤53mm |  |
|  |  | 2 | 形位公差 | 030704 | 滚动轴承零件 球面滚子技术条件 CSBTS TC98.69-1999 5.2,6.2.1,6.2.2,6.2.3 |  |  |
| 23 | 冲压保持架 | 1 | 尺寸公差 | 030704 | 滚动轴承 冲压保持架 技术条件 GB/T 28268-2012 6.3,7 | 只测: 20mm≤d≤100mm ，30mm≤D≤215mm |  |
|  |  | 2 | 径向游动量 | 030704 | 滚动轴承 冲压保持架 技术条件 GB/T 28268-2012 7 | 只测: 52mm≤D≤200mm |  |
|  |  | 3 | 翘曲度 | 030704 | 滚动轴承 冲压保持架 技术条件 GB/T 28268-2012 6.3,7 | 只测: 52mm≤D≤200mm |  |
| 24 | 实体保持架 | 1 | 尺寸公差 | 030704 | 滚动轴承零件 金属实体保持架 技术条件 JB/T 11841-2014 6.2,7 | 只测:30mm≤D≤300mm |  |
| 25 | 热处理高碳铬轴承钢滚动轴承零件 | 1 | 布氏硬度 | 030103 | 高碳铬轴承钢零件 热处理技术条件 JB/T 1255-2014 4 | 只测：HBW10/3000,HBW10/1000,HBW5/75O,HBW5/250 |  |
|  |  | 2 | 洛氏硬度 | 030103 | 高碳铬轴承钢零件 热处理技术条件 JB/T 1255-2014 4 | 只测:HRC |  |
|  |  | 3 | 脱碳层深度 | 030202 | 高碳铬轴承钢零件 热处理技术条件 JB/T 1255-2014 4 | 只用：金相法 |  |
|  |  | 4 | 显微组织 | 030204 | 高碳铬轴承钢零件 热处理技术条件 JB/T 1255-2014 4 |  |  |
|  |  | 5 | 网状碳化物 | 030204 | 高碳铬轴承钢零件 热处理技术条件 JB/T 1255-2014 4 |  |  |
|  |  | 6 | 回火稳定性 | 030103 | 高碳铬轴承钢零件 热处理技术条件 JB/T 1255-2014 4 |  |  |
|  |  | 7 | 钢球压碎载荷 | 030199 | 高碳铬轴承钢零件 热处理技术条件 JB/T 1255-2014 4 | 只测：2000kN以下 |  |
| 26 | 渗碳热处理滚动轴承零件 | 1 | 洛氏硬度 | 030103 | 滚动轴承 零件渗碳热处理 技术条件 JB/T 8881-2011 5 | 只测:HRC |  |
|  |  | 2 | 碳化物 | 030204 | 滚动轴承 零件渗碳热处理 技术条件 JB/T 8881-2011 5 |  |  |
|  |  | 3 | 显微组织 | 030204 | 滚动轴承 零件渗碳热处理 技术条件 JB/T 8881-2011 5 |  |  |
|  |  | 4 | 淬硬层深度 | 030202 | 滚动轴承零件渗碳热处理技术条件 JB/T8881-2011 5 | 不测：宏观断口法 |  |
|  |  | 5 | 表面碳含量 | 020102 | 碳素钢和中低合金钢 多元素含量的测定 火花放电原子发射光谱法(常规法) GB/T 4336-2016 |  |  |
| 27 | 热处理高碳铬不锈钢滚动轴承零件 | 1 | 显微组织 | 030204 | 滚动轴承 高碳铬不锈钢轴承零件 热处理技术条件 JB/T 1460-2011 4 |  |  |
|  |  | 2 | 洛氏硬度 | 030103 | 滚动轴承 高碳铬不锈钢轴承零件 热处理技术条件 JB/T 1460-2011 4 | 只测:HRC |  |
|  |  | 3 | 钢球压碎载荷 | 030199 | 滚动轴承 高碳铬不锈钢轴承零件 热处理技术条件 JB/T 1460-2011 4 | 只测：2000kN以下 |  |
| 28 | 热处理Cr4Mo4V高温轴承钢零件 | 1 | 显微组织 | 030204 | 滚动轴承 Cr4Mo4V高温轴承钢零件 热处理技术条件 JB/T 2850-2007 4 |  |  |
|  |  | 2 | 洛氏硬度 | 030103 | 滚动轴承 Cr4Mo4V高温轴承钢零件 热处理技术条件 JB/T 2850-2007 4 | 只测:HRC |  |
|  |  | 3 | 钢球压碎载荷 | 030199 | 滚动轴承 Cr4Mo4V高温轴承钢零件 热处理技术条件 JB/T 2850-2007 4 | 只测：2000kN以下 |  |
| 29 | 机械零部件（几何尺寸） | 1 | 圆度 | 030704 | 滚动轴承零件 圆度和波纹度误差测量及评定方法 GB/T 32324-2015 4.1.3,6.1.1 |  |  |
|  |  |  |  |  | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.3 |  |  |
|  |  | 2 | 粗糙度 | 030704 | 滚动轴承零件 表面粗糙度测量和评定方法 JB/T 7051-2006 5.1,5.2,5.3,5.4,6.1 |  |  |
|  |  | 3 | 尺寸 | 030704 | 产品几何技术规范(GPS) 光滑工件尺寸的检验 GB/T 3177-2009 |  |  |
|  |  | 4 | 直线度 | 030704 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.1 |  |  |
|  |  | 5 | 平面度 | 030704 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.2 |  |  |
|  |  | 6 | 圆柱度 | 030704 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.4 |  |  |
|  |  | 7 | 平行度 | 030704 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.7 |  |  |
|  |  | 8 | 垂直度 | 030704 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.8 |  |  |
|  |  | 9 | 倾斜度 | 030704 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.9 |  |  |
|  |  | 10 | 同轴度 | 030704 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.10 |  |  |
|  |  | 11 | 位置度 | 030704 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.12 |  |  |
|  |  | 12 | 对称度 | 030704 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.11 |  |  |
|  |  | 13 | 圆跳动 | 030704 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.13 |  |  |
|  |  | 14 | 全跳动 | 030704 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.14 |  |  |
| 30 | 金属材料及金属制件 | 1 | 拉伸试验 | 030101 | 金属材料 拉伸试验 第1部分:室温试验方法 GB/T 228.1-2010 7,8,10,11,12,13,20,21,22 | 只测:600kN以下,方法B的Rm,A,Z,ReL和Rp |  |
|  |  | 2 | 冲击试验 | 030104 | 金属材料 夏比摆錘冲击试验方法 GB/T 229-2007 8 | 只测:室温至-40℃,300J以下的KV2 |  |
|  |  | 3 | 洛氏硬度 | 030103 | 金属材料 洛氏硬度试验 第1部分:试验方法 GB/T 230.1-2009 7,9 | 只测:HRC |  |
|  |  | 4 | 维氏硬度 | 030103 | 金属材料 维氏硬度试验 第1部分:试验方法 GB/T 4340.1-2009 7 | 只测:HV1 |  |
|  |  | 5 | 布氏硬度 | 030103 | 金属材料 布氏硬度试验 第1部分:试验方法 GB/T231.1-2009 7 | 只测：HBW10/3000,HBW10/1000,HBW5/75O,HBW5/250 |  |
|  |  | 6 | 晶粒度 | 030201 | 金属平均晶粒度测定方法 GB/T 6394-2002 5.1 | 只用:比较法 |  |
|  |  | 7 | 显微组织 | 030204 | 钢的显微组织评定方法 GB/T 13299-1991 4,5 | 只测:游离渗碳体和带状组织 |  |
|  |  | 8 | 非金属夹杂物 | 030203 | 钢中非金属夹杂物含量的测定 标准评级图显微检验法 GB/T 10561-2005 5.2.1 | 只用:A法 |  |
|  |  | 9 | 低倍组织 | 030205 | 钢的低倍组织及缺陷酸蚀检验法 GB/T 226-2015 4.2 | 只用:热酸腐蚀法 |  |
|  |  | 10 | 脱碳层深度 | 030202 | 钢的脱碳层深度测定法 GB/T 224-2008 4.2 | 只用:金相法 |  |
|  |  |  |  |  | 滚动轴承 零件脱碳层深度测定法 JB/T7362-2007 4.1 | 只用：金相法 |  |
|  |  | 11 | 碳化物不均匀度 | 030204 | 钢的共晶碳化物不均匀度评定法 GB/T 14979-1994 4.2,4.3,4.4,5 |  |  |
|  |  | 12 | 碳,硫 | 020108 | 钢铁 总碳硫含量的测定 高频感应炉燃烧后红外吸收法(常规方法) GB/T 20123-2006 |  |  |
|  |  | 13 | 碳,硫,硅,锰,磷,铬,镍,钼,铜,铝，砷，锡，钛 | 020102 | 碳素钢和中低合金钢 多元素含量的测定 火花放电原子发射光谱法(常规法) GB/T 4336-2016 |  |  |
|  |  | 14 | 碳，硫，硅，锰，磷，铬，镍，钼，铜,铝，钛 | 020102 | 不锈钢 多元素含量的测定 火花放电原子发射光谱法(常规法) GB/T 11170-2008 |  |  |
|  |  | 15 | 钙 | 020102 | 碳钢和低合金钢分析火花原子发射光谱法 ASTM E415-2015 |  |  |
|  |  | 16 | 硅，锰，磷，镍，铬，钼，铜，铝，钛 | 020101 | 低合金钢 多元素含量的测定 电感耦合等离子体原子发射光谱法 GB/T20125-2006 |  |  |
|  |  | 17 | 硅，锰，磷，镍，铬，钼，铜，钛 | 020101 | 不锈钢化学成分测定电感耦合等离子体原子发射光谱法 SN/T2718-2010 |  |  |
|  |  | 18 | 硅，锰，磷，铬，镍，铝，铅，锡 | 020101 | 铜及铜合金化学分析方法第27部分:电感耦合等离子体体原子发射光谱法 GB/T 5121.27-2008 |  |  |
|  |  | 19 | 铜 | 020114 | 黄铜中铜量的测定 碘量法 YS/T910-2013 |  |  |
|  |  | 20 | 氧 | 020109 | 钢铁 氧含量的测定 脉冲加热惰气熔融-红外线吸收法 GB/T 11261-2006 |  |  |
|  |  | 21 | 氮 | 020109 | 钢铁 氮含量的测定 惰性气体熔融热导法（常规方法） GB/T 20124-2006 |  |  |
|  |  | 22 | *超声检测 | 110202 | 钢锻件超声检测方法 GB/T 6402-2008 |  |  |
|  |  |  |  |  | 锻轧钢棒超声检测方法 GB/T 4162-2008 |  |  |
|  |  | 23 | 磁粉检测 | 110203 | 滚动轴承 无损检测 磁粉检测 GB/T 24606-2009 |  |  |
|  |  |  |  |  | 机车车辆轮对滚动轴承磁粉探伤方法 TB/T 1987-2003 |  |  |
|  |  | 24 | *渗透检测 | 110204 | 无损检测 渗透检测方法 JB/T 9218-2015 |  |  |
| 31 | 高碳铬不锈钢 | 1 | 非金属夹杂物 | 030203 | 高碳铬不锈轴承钢 GB/T 3086-2008 7 | 只用:A法 |  |
|  |  | 2 | 显微组织 | 030204 | 高碳铬不锈轴承钢 GB/T 3086-2008 7 |  |  |
|  |  | 3 | 碳化物不均匀度 | 030204 | 高碳铬不锈轴承钢 GB/T 3086-2008 7 |  |  |
|  |  | 4 | 脱碳层深度 | 030202 | 高碳铬不锈轴承钢 GB/T 3086-2008 7 | 只用:金相法 |  |
|  |  | 5 | 低倍 | 030205 | 高碳铬不锈轴承钢 GB/T 3086-2008 7 | 只用:热酸腐蚀法 |  |
|  |  | 6 | 碳,硫 | 020108 | 钢铁 总碳硫含量的测定 高频感应炉燃烧后红外吸收法(常规方法) GB/T 20123-2006 |  |  |
|  |  | 7 | 磷,硅,铬,钼,锰,镍,铜 | 020102 | 碳素钢和中低合金钢 多元素含量的测定 火花放电原子发射光谱法(常规法) GB/T 4336-2016 |  |  |
| 32 | 渗碳轴承钢 | 1 | 晶粒度 | 030201 | 渗碳轴承钢 技术条件 GB3203-82 3 | 只用:比较法 |  |
|  |  | 2 | 显微组织 | 030204 | 渗碳轴承钢 技术条件 GB3203-82 3 |  |  |
|  |  | 3 | 非金属夹杂物 | 030203 | 渗碳轴承钢 技术条件 GB3203-82 3 | 只用:A法 |  |
|  |  | 4 | 低倍 | 030205 | 渗碳轴承钢 技术条件 GB3203-82 3 | 只用:热酸腐蚀法 |  |
|  |  | 5 | 布氏硬度 | 030103 | 渗碳轴承钢 技术条件 GB/T 3203-82 3 | 只测：HBW10/3000,HBW10/1000,HBW5/75O,HBW5/250 |  |
|  |  | 6 | 碳,硫 | 020108 | 钢铁 总碳硫含量的测定 高频感应炉燃烧后红外吸收法(常规方法) GB/T 20123-2006 |  |  |
|  |  | 7 | 硅,锰,铬,镍,钼,铜,磷 | 020101 | 低合金钢 多元素含量的测定 电感耦合等离子体原子发射光谱法 GB/T20125-2006 |  |  |
|  |  | 8 | 碳，硫，硅,锰,铬,镍,钼,铜,磷 | 020102 | 碳素钢和中低合金钢 多元素含量的测定 火花放电原子发射光谱法(常规法) GB/T 4336-2016 |  |  |
| 33 | 高碳铬轴承钢 | 1 | 非金属夹杂物 | 030203 | 高碳铬轴承钢 GB/T 18254-2002 6.6 | 只用:A法 |  |
|  |  |  |  |  | 高碳铬轴承钢丝 GB/T 18579-2001 6.6 |  |  |
|  |  | 2 | 显微组织 | 030204 | 高碳铬轴承钢 GB/T 18254-2002 6.7 |  |  |
|  |  |  |  |  | 高碳铬轴承钢丝 GB/T 18579-2001 6.6 |  |  |
|  |  | 3 | 碳化物不均匀性 | 030204 | 高碳铬轴承钢 GB/T 18254-2002 6.8 |  |  |
|  |  |  |  |  | 高碳铬轴承钢丝 GB/T 18579-2001 7.8 |  |  |
|  |  | 4 | 显微孔隙 | 030204 | 高碳铬轴承钢 GB/T 18254-2002 6.9 |  |  |
|  |  |  |  |  | 高碳铬轴承钢丝 GB/T 18579-2001 7.8 |  |  |
|  |  | 5 | 脱碳层深度 | 030202 | 高碳铬轴承钢 GB/T 18254-2002 6.5 | 只用:金相法 |  |
|  |  |  |  |  | 高碳铬轴承钢丝 GB/T 18579-2001 6.6 |  |  |
|  |  | 6 | 低倍 | 030205 | 高碳铬轴承钢 GB/T 18254-2002 6.4 | 只用:热酸腐蚀法 |  |
|  |  |  |  |  | 高碳铬轴承钢丝 GB/T 18579-2001 7.8 |  |  |
|  |  | 7 | 布氏硬度 | 030103 | 高碳铬轴承钢 GB/T 18254-2002 6.11 | 只测：HBW10/3000,HBW10/1000,HBW5/75O,HBW5/250 |  |
|  |  | 8 | 拉伸试验 | 030101 | 高碳铬轴承钢丝 GB/T 18579-2001 6.5 | 只测:600kN以下,方法B的Rm,A,Z,ReL和Rp |  |
|  |  | 9 | 碳,硫 | 020108 | 钢铁 总碳硫含量的测定 高频感应炉燃烧后红外吸收法(常规方法) GB/T 20123-2006 |  |  |
|  |  | 10 | 碳，硫，磷,硅,铬,钼,锰,镍,铜 | 020102 | 碳素钢和中低合金钢 多元素含量的测定 火花放电原子发射光谱法(常规法) GB/T 4336-2016 |  |  |
| 34 | 冷轧钢板钢带 | 1 | 拉伸试验 | 030101 | 优质碳素结构钢冷轧钢板和钢带 GB/T13237-2013 7 | 只测:600kN以下,方法B的Rm,A,Z,ReL和Rp |  |
|  |  | 2 | 晶粒度 | 030201 | 优质碳素结构钢冷轧钢板和钢带 GB/T13237-2013 7 | 只用:比较法 |  |
|  |  | 3 | 游离渗碳体 | 030204 | 优质碳素结构钢冷轧钢板和钢带 GB/T13237-2013 7 |  |  |
|  |  | 4 | 碳,硫 | 020108 | 钢铁 总碳硫含量的测定 高频感应炉燃烧后红外吸收法(常规方法) GB/T 20123-2006 |  |  |
|  |  | 5 | 硅,锰,磷,铬,镍,铜,铝 | 020101 | 低合金钢 多元素含量的测定 电感耦合等离子体原子发射光谱法 GB/T20125-2006 |  |  |
|  |  | 6 | 碳，硫，硅,锰,磷,铬,镍,铜,铝 | 020102 | 碳素钢和中低合金钢 多元素含量的测定 火花放电原子发射光谱法(常规法) GB/T 4336-2016 |  |  |
| 35 | 热轧钢板钢带 | 1 | 拉伸试验 | 030101 | 优质碳素结构钢热轧厚钢板和钢带 GB/T711-2008 7 | 只测:600kN以下,方法B的Rm,A,Z,ReL和Rp |  |
|  |  | 2 | 碳,硫 | 020108 | 钢铁 总碳硫含量的测定 高频感应炉燃烧后红外吸收法(常规方法) GB/T 20123-2006 |  |  |
|  |  | 3 | 硅,锰,磷,铬,镍,铜 | 020101 | 低合金钢 多元素含量的测定 电感耦合等离子体原子发射光谱法 GB/T20125-2006 |  |  |
|  |  | 4 | 碳，硫，硅,锰,磷,铬,镍,铜 | 020102 | 碳素钢和中低合金钢 多元素含量的测定 火花放电原子发射光谱法(常规法) GB/T 4336-2016 |  |  |
| 36 | 铜及铜合金挤制管 | 1 | 拉伸试验 | 030101 | 铜及铜合金挤制管 YS/T662-2007 4..3 | 只测:600kN以下,方法B的Rm,A,Z,ReL和Rp |  |
|  |  | 2 | 布氏硬度 | 030103 | 铜及铜合金挤制管 YS/T662-2007 4.3 | 只测：HBW10/3000,HBW10/1000,HBW5/75O,HBW5/250 |  |
| 37 | 合金钢锻件 | 1 | 拉伸试验 | 030101 | 大型合金钢锻件技术条件 JB/T6396-2006 5.2 | 只测:600kN以下,方法B的Rm,A,Z,ReL和Rp |  |
|  |  | 2 | 冲击试验 | 030104 | 大型合金钢锻件技术条件 JB/T6396-2006 5.2 | 只测:室温至-40℃,300J以下的KV2 |  |
| 38 | 润滑脂 | 1 | 滴点 | 021002 | 润滑脂滴点测定法 GB/T4929-1985 |  |  |
|  |  | 2 | 锥入度 | 021002 | 润滑脂和石油脂锥入度测定法 GB/T269-1991 | 只用全尺寸锥体方法 |  |
| 39 | 润滑油 | 1 | 运动粘度 | 021003 | 石油产品运动粘度测定法和动力粘度计算法 GB/T 265-1988 | 40℃、100℃的运动粘度 |  |
|  |  | 2 | 闪点(开口) | 021003 | 石油产品 闪点和燃点的测定克利夫兰开口杯法 GB/T 3536-2008 |  |  |

组长/组员签字：

附表3-1                                                 任务编号：L21135-2016-01

推荐认可的实验室检测能力范围（英文）

Lab：Test Center of Luoyang LYC Bearing Co,Ltd

Add：No.96,Jianshe Road,Jianxi District,Luoyang City,China

| №. | Test object | Item/ Parameter | Code of field | Title， Code of standard or method | Note | Expansion or change |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | №. | Item/ Parameter |  |  |  |  |
| 1 | Rolling bearing (parameter) | 1 | Dimensional tolerance and rotation accuracy | 030704 | Rolling bearings－Measuring and gauging principles and methods GB/T 307.2-2005 7,8,9,10,11,12，13,14,15 | Accredited only for:12mm≤d≤1000mm,30mm≤D≤1400mm |  |
|  |  |  |  |  | Rolling bearings--Radial bearings--Tolerances GB/T 307.1-2005 5.1,5.2,5.3,5.4 |  |  |
|  |  |  |  |  | Rolling bearings—Tolerances—Part 4:Tolerances for thrust bearings GB/T 307.4-2012 5.2,5.3,5.4,5.5 |  |  |
|  |  |  |  |  | Rolling bearings and parts-Supplementary specifications JB/T 10336-2002 4.1.1.3,4.1.1.4,4.2.1.2,4.2.1.4,4.2.1.5,4.2.1.5,4.2.1.7 |  |  |
|  |  | 2 | end play | 030704 | Rolling bearings - Measuring methods for radial internal clearance GB/T 25769-2010 6,7,8,9 | Accredited only for:32mm≤D≤1000mm |  |
|  |  |  |  |  | Rolling bearings-Internal clearances and adjusting methods for double-row and four-row tapered roller bearings JB/T 8236-2010 4,5 |  |  |
|  |  |  |  |  | Rolling bearings - Insert bearings - Radial internal clearance GB/T 25766-2010 6.1,7 |  |  |
|  |  |  |  |  | Rolling bearings—Internal clearance—Part 1:Radial internal clearance for radial bearings GB/T 4604.1-2012 5 |  |  |
|  |  |  |  |  | Rolling bearings—Internal clearance—Part 2:Axial internal clearance for four-point-contact ball bearings GB/T4604.2-2013 5 |  |  |
|  |  | 3 | residual magnetism | 030704 | Rolling bearings—Residual magnetism and its assessment method JB/T 6641-2007 5 | Accredited only for:≤10mT |  |
|  |  | 4 | cleanliness | 030704 | Rolling bearings—Assesment methods for cleanliness JB/T 7050-2005 7 | Accredited only for:foreign substance≤200mg |  |
|  |  | 5 | vibration | 030704 | Rolling bearings—Measuring methods for vibration—Part 1:Fundamentals GB/T 24610.1-2009 6 | Accredited only for:30mm≤D≤200mm |  |
|  |  |  |  |  | Rolling bearings—Measuring methods for vibration—Part 2:Radial ball bearings with cylindrical bore and outside surface GB/T 24610.2-2009 5 |  |  |
|  |  |  |  |  | Rolling bearings—Measuring methods for vibration—Part 3:Radial spherical and tapered roller bearings with cylindrical bore and outside surface GB/T 24610.3-2009 5 |  |  |
|  |  |  |  |  | Rolling bearings—Measuring methods for vibration—Part 4:Radial cylindrical roller bearings with cylindrical bore and outside surface GB/T 24610.4-2009 5 |  |  |
|  |  |  |  |  | Rolling bearings — Specifications for vibration（velocity）of deep groove ball bearings GB/T 32325-2015 6 |  |  |
|  |  |  |  |  | Rolling bearings ― Specifications for vibration（velocity）of cylindrical roller bearings JB/T8922-2011 4 |  |  |
|  |  |  |  |  | Rolling bearings — Specifications of vibration（velocity） for tapered roller bearings JB/T10236-2014 6 |  |  |
|  |  |  |  |  | Rolling bearings — Specifications of vibration（acceleration） for tapered roller bearings JB/T 10237-2014 6 |  |  |
|  |  |  |  |  | Rolling bearings-Measuring methods for vibration(acceleration) GB/T 32333-2015 6 |  |  |
|  |  | 6 | extrinsic feature | 030704 | Rolling bearings—Marking for products GB/T 24605-2009 7 |  |  |
|  |  |  |  |  | Rolling bearings—Rust proof packaging GB/T 8597-2013 4.2.4,4.1,4.3.2,4.3.3,4.4 |  |  |
|  |  |  |  |  | Rolling bearings and parts-Supplementary specifications JB/T10336-2002 4.1.1.5,4.1.1.6,4.1.1.7,4.1.1.8,4.1.1.9,4.1.1.10,4.1.1.11,4.1.2.1,4.1.2.2,4.2.2.1,4.2.2.2 |  |  |
|  |  |  |  |  | Rolling bearing rings and roller parts appearance quality requirements CSBTS TC98.54-1999 4,5,6 |  |  |
|  |  | 7 | life test | 030704 | Rolling bearings—Test and assessment for life and reliability GB/T 24607-2009 |  |  |
|  |  |  |  |  | Endurance test method for axle box rolling bearing of rolling stock on axle box test machine TB/T 3017-2001 | Accredited only for:100mm≤d≤180mm |  |
| 2 | turntable bearings | 1 | *tolerance of dimension | 030704 | Rolling bearings-Slewing bearings JB/T10471-2004 6.5.1 | Accredited only for:200mm≤D≤6300mm；Except for:gear parameters |  |
|  |  | 2 | *running accuracy | 030704 | Rolling bearings-Slewing bearings JB/T10471-2004 6.5.2,7.1 | Accredited only for:200mm≤D≤6300mm |  |
|  |  | 3 | *end play | 030704 | Rolling bearings-Slewing bearings JB/T10471-2004 6.8,7.3 | Accredited only:200mm≤D≤6300mm |  |
| 3 | Wind turbine yaw, variable pitch bearing | 1 | *dimensional tolerance | 030704 | Rolling bearings—Wind power generators yaw and pitch bearings GB/T29717-2013 7.3.1 | Accredited only for:200mm≤D≤6300mm；Except for:gear parameters |  |
|  |  | 2 | *running accuracy | 030704 | Rolling bearings—Wind power generators yaw and pitch bearings GB/T29717-2013 7.3.2 | Accredited only for:200mm≤D≤6300mm |  |
|  |  | 3 | *end play | 030704 | Rolling bearings—Wind power generators yaw and pitch bearings GB/T29717-2013 7.5 | Accredited only for:200mm≤D≤6300mm |  |
| 4 | Blower bearing | 1 | dimensional tolerance | 030704 | Rolling bearings－Blowers bearings－Specifications JB/T 7753-2007 3.2,4.1 |  |  |
|  |  | 2 | running accuracy | 030704 | Rolling bearings－Blowers bearings－Specifications JB/T 7753-2007 3.2,4.1 |  |  |
| 5 | Needle roller and double direction thrust cylindrical roller bearing | 1 | dimensional tolerance | 030704 | Rolling bearings - Combined needle roller bearings with double direction thrust cylindrical roller bearings GB/T 25768-2010 7.2 |  |  |
|  |  | 2 | running accuracy | 030704 | Rolling bearings - Combined needle roller bearings with double direction thrust cylindrical roller bearings GB/T 25768-2010 7.2 |  |  |
| 6 | Machine tool bearings | 1 | dimensional tolerance | 030704 | Rolling bearings—Angular contact thrust ball bearings used for machine tool screws GB/T 24604-2009 7.2 |  |  |
|  |  |  |  |  | Rolling Bearings--Double-direction angular contact thrust ball bearings for machine-tool spindle JB/T6362-2007 7,8.1,8.2 |  |  |
|  |  |  |  |  | Rolling bearings—Cylindrical roller bearings for spindles of machines GB/T 27559-2011 7.2,8.1 |  |  |
|  |  | 2 | running accuracy | 030704 | Rolling Bearings-Double-direction angular contact thrust ball bearings for machine-tool spindle JB/T6362-2007 7 |  |  |
|  |  |  |  |  | Rolling bearings—Cylindrical roller bearings for spindles of machines GB/T 27559-2011 7.2,8.1 |  |  |
|  |  | 3 | end play | 030704 | Rolling bearings—Cylindrical roller bearings for spindles of machines GB/T 27559-2011 7.5,8.3 |  |  |
| 7 | Thin wall sealing bearing for robot | 1 | dimensional tolerance | 030704 | Rolling bearings—Thin section sealed bearings for robots JB/T 6636-2007 6.1,7.1 |  |  |
|  |  | 2 | end play | 030704 | Rolling bearings—Thin section sealed bearings for robots JB/T 6636-2007 6.5 |  |  |
| 8 | Automobile generator bearing | 1 | dimensional tolerance | 030704 | Rolling bearings-Alternator bearings for automotive-Specifications JB/T 8167-2006 2 |  |  |
|  |  | 2 | running accuracy | 030704 | Rolling bearings-Alternator bearings for automotive-Specifications JB/T 8167-2006 2 |  |  |
|  |  | 3 | end play | 030704 | Rolling bearings-Alternator bearings for automotive-Specifications JB/T 8167-2006 3.6 |  |  |
|  |  | 4 | vibration | 030704 | Rolling bearings-Alternator bearings for automotive-Specifications JB/T 8167-2006 3.7 |  |  |
| 9 | Automobile wheel hub bearing unit | 1 | end play | 030704 | Rolling bearings－Automotive hub bearing units JB/T 10238-2011 9.4 |  |  |
| 10 | deep groove ball bearing | 1 | end play | 030704 | Rolling bearings—Deep groove ball bearings for electric motors—Specifications GB/T 28698-2012 5.6,6.3 |  |  |
|  |  | 2 | Grease filling amount | 030704 | Rolling Bearings—Sealed deep groove ball bearings—Specifications JB/T 7752-2005 4.5 | Accredited only for:≤200g |  |
| 11 | thrust bearing | 1 | dimensional tolerance | 030704 | Rolling bearings--Self-aligning thrust roller bearings--Specification JB/T 7750-2007 4.2,5.1 |  |  |
|  |  |  |  |  | Rolling bearings—Thrust cylindrical roller and cage assemblies,thrust washers JB/T 8211-2005 6.2,7.1 |  |  |
|  |  |  |  |  | Rolling bearings—Thrust tapered roller bearings JB/T 7751-2016 7.2,8.1 |  |  |
| 12 | Supporting supporting contact ball bearing | 1 | dimensional tolerance | 030704 | Rolling bearings-Specifications for matched angular contace ball bearings JB/T 10186-2010 6.1.4,appendixA |  |  |
|  |  | 2 | running accuracy | 030704 | Rolling bearings-Specifications for matched angular contace ball bearings JB/T 10186-2010 6.1.3, appendixA |  |  |
| 13 | Boutique bearing | 1 | dimensional tolerance | 030704 | Boutique bearing－Specification CSBTS TC98.76-2001 2,7.1 |  |  |
|  |  | 2 | running accuracy | 030704 | Boutique bearing－Specification CSBTS TC98.76-2001 2 |  |  |
|  |  | 3 | end play | 030704 | Boutique bearing－Specification CSBTS TC98.76-2001 6.5 |  |  |
|  |  | 4 | vibration | 030704 | Boutique bearing－Specification CSBTS TC98.76-2001 6.6.1,6.6.3 |  |  |
| 14 | railway bearing | 1 | dimensional tolerance | 030704 | Rolling bearing in the railway passenger car and wayon TB/T2235-2010 2,5.6 |  |  |
|  |  |  |  |  | Rolling bearings - Bearings for railway passenger coach GB/T25772-2010 8.2,9.2 |  |  |
|  |  |  |  |  | Rolling bearings - Bearings for railway locomotive GB/T25771-2010 9.2,10.2 |  |  |
|  |  |  |  |  | Rolling bearings - Bearings for railway wagon GB/T25770-2010 8.2,9.2 |  |  |
|  |  | 2 | running accuracy | 030704 | Rolling bearing in the railway passenger car and wayon TB/T2235-2010 2,5.6 |  |  |
|  |  |  |  |  | Rolling bearings - Bearings for railway passenger coach GB/T25772-2010 8.2,9.2 |  |  |
|  |  |  |  |  | Rolling bearings - Bearings for railway locomotive GB/T25771-2010 9.2,10.2 |  |  |
|  |  |  |  |  | Rolling bearings - Bearings for railway wagon GB/T25770-2010 8.2,9.2 |  |  |
|  |  | 3 | end play | 030704 | Rolling bearing in the railway passenger car and wayon TB/T2235-2010 4.2.1 |  |  |
|  |  |  |  |  | Rolling bearings - Bearings for railway passenger coach GB/T25772-2010 8.3,9.3 |  |  |
|  |  |  |  |  | Rolling bearings - Bearings for railway locomotive GB/T25771-2010 9.3,10.3 |  |  |
| 15 | Flange ring radial ball bearing | 1 | dimensional tolerance | 030704 | Rolling bearings—Radial ball bearings with flanged outer ring—Flange dimensions GB/T7217-2013 5 |  |  |
| 16 | cylindrical roller bearing | 1 | dimensional tolerance | 030704 | Rolling bearings--Double row full complement cylindrical roller bearing track rollers JB/T 7754-2007 8.2,9.1 |  |  |
| 17 | Rolling mill bearing | 1 | dimensional tolerance | 030704 | Rolling bearings—Double row and four row tapered roller bearings for rolling mills JB/T 5389.2-2005 6.1,7.1 |  |  |
|  |  |  |  |  | Rolling bearings—Roller bearings for rolling mills —Part 1:Four-row cylindrical roller bearings JB/T 5389.1-2016 7.2,8.1 |  |  |
|  |  |  |  |  | Rolling bearings—Full complement taperred roller thrust bearings for rolling mill screw-down mechanisms JB/T 3632-2015 8.2,9.1 |  |  |
|  |  | 2 | running accuracy | 030704 | Rolling bearings—Double row and four row tapered roller bearings for rolling mills JB/T 5389.2-2005 6.1 |  |  |
|  |  |  |  |  | Rolling bearings—Roller bearings for rolling mills —Part 1:Four-row cylindrical roller bearings JB/T 5389.1-2016 7.2 |  |  |
|  |  | 3 | end play | 030704 | Rolling bearings—Double row and four row tapered roller bearings for rolling mills JB/T 5389.2-2006 7.2 |  |  |
|  |  | 4 | residual magnetism | 030704 | Rolling bearings—Full complement taperred roller thrust bearings for rolling mill screw-down mechanisms JB/T 3632-2015 8.4,9.5 | Accredited only for:≤10mT |  |
| 18 | Rolling bearing parts (parameters) | 1 | circular degree | 030704 | Rolling bearing parts -Methods for measurement and assessment departure from roundness and waviness GB/T 32324-2015 4.1.3,6.1.1 | Accredited only for:D≤400mm |  |
|  |  |  |  |  | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.3 |  |  |
|  |  | 2 | roughness | 030704 | Rolling bearing parts-Methods for the measurement and assessment of surface roughness JB/T 7051-2006 5.1,5.2,5.3,5.4,6.1 | Accredited only for:D≤400mm |  |
| 19 | steel ball | 1 | dimensional tolerance | 030704 | Rolling bearings—Balls—Part 1:Steel balls GB/T 308.1-2013 6.5,7.1 | Accredited only for:6mm≤Dw≤53mm |  |
|  |  | 2 | Spherical error | 030704 | Rolling bearings—Balls—Part 1:Steel balls GB/T 308.1-2013 6.4,7.2 | Accredited only for:6mm≤Dw≤53mm |  |
|  |  | 3 | extrinsic feature | 030704 | Rolling bearings—Atlas and the assessment methods for surface imperfections of steel balls JB/T10861-2008 4 |  |  |
|  |  | 4 | Steel ball vibration | 030704 | Rolling bearings-Specifications for vibration (acceleration) of steel balls JB/T 8923-2010 5,6 | Accredited only for:5mm≤Dw≤30mm |  |
| 20 | cylindrical roller | 1 | dimensional tolerance | 030704 | Rolling bearings—Cylindrical rollers GB/T 4661-2015 6.3,7.1,7.3,7.5 | Accredited only for:10mm≤Dw≤53mm |  |
|  |  | 2 | geometric tolerance | 030704 | Rolling bearings—Cylindrical rollers GB/T 4661-2015 6.3,7.2,7.4 |  |  |
| 21 | tapered roller | 1 | dimensional tolerance | 030704 | Rolling bearings - Tapered rollers GB/T 25767-2010 6.2.2,7.1.1,7.1.2 | Accredited only for:6mm≤Dw≤70mm |  |
|  |  | 2 | geometric tolerance | 030704 | Rolling bearings - Tapered rollers GB/T 25767-2010 6.2.2,7.1.3,7.1.4,7.1.5,7.3.1, |  |  |
| 22 | spherical roller | 1 | dimensional tolerance | 030704 | Rolling bearing parts-Spherical roller -Specification CSBTS TC98.69-1999 6.2.1,6.2.2,6.2.3,5.1,5.2 | Accredited only for:10mm≤Dw≤53mm |  |
|  |  | 2 | geometric tolerance | 030704 | Rolling bearing parts-Spherical roller -Specification CSBTSTC98.69-1999 5.2,6.2.1,6.2.2,6.2.3 |  |  |
| 23 | Pressed Cage | 1 | dimensional tolerance | 030704 | Rolling bearings—Specifications of pressed cages GB/T 28268-2012 6.3,7 | Accredited only for:20mm≤d≤100mm,30mm≤D≤215mm |  |
|  |  | 2 | Radial mobility | 030704 | Rolling bearings—Specifications of pressed cages GB/T 28268-2012 7 | Accredited only for:52mm≤D≤200mm |  |
|  |  | 3 | warping degree | 030704 | Rolling bearings—Specifications of pressed cages GB/T 28268-2012 6.3,7 | Accredited only for:52mm≤D≤200mm |  |
| 24 | solid cage | 1 | dimensional tolerance | 030704 | Rolling bearing parts－Metal solid cages－Specifications JB/T 11841-2014 6.2,7 | Accredited only for:30mm≤D≤300mm |  |
| 25 | Heat treaed high carbon chromium bearing steel parts | 1 | Brinell hardness | 030103 | Rolling bearings - Parts made from high- carbon chromium bearing steels-Specifications for heat treatment JB/T 1255-2014 4 | Accredited only for:HBW10/3000,HBW10/1000,HBW5/75O,HBW5/250 |  |
|  |  | 2 | Rockwell hrdness | 030103 | Rolling bearings - Parts made from high- carbon chromium bearing steels-Specifications for heat treatment JB/T 1255-2014 4 | Accredited only for:HRC |  |
|  |  | 3 | The depth of decarburization layer | 030202 | Rolling bearings - Parts made from high- carbon chromium bearing steels-Specifications for heat treatment JB/T 1255-2014 4 | Accredited only for:Metallographic method |  |
|  |  | 4 | The microstructure | 030204 | Rolling bearings - Parts made from high- carbon chromium bearing steels-Specifications for heat treatment JB/T 1255-2014 4 |  |  |
|  |  | 5 | Carbide network | 030204 | Rolling bearings - Parts made from high- carbon chromium bearing steels-Specifications for heat treatment JB/T 1255-2014 4 |  |  |
|  |  | 6 | Tempering stability | 030103 | Rolling bearings - Parts made from high- carbon chromium bearing steels-Specifications for heat treatment JB/T 1255-2014 4 |  |  |
|  |  | 7 | Steel ball crushing load | 030199 | Rolling bearings - Parts made from high- carbon chromium bearing steels-Specifications for heat treatment JB/T 1255-2014 4 | Accredited only for:≤2000kN |  |
| 26 | Carburizing heat treated rolling bearing components | 1 | Rockwell hardness | 030103 | Rolling bearings－Carburizing heat-treatment for parts－Specifications JB/T 8881-2011 5 | Accredited only for:HRC |  |
|  |  | 2 | Carbide | 030204 | Rolling bearings－Carburizing heat-treatment for parts－Specifications JB/T 8881-2011 5 |  |  |
|  |  | 3 | The microstructure | 030204 | Rolling bearings－Carburizing heat-treatment for parts－Specifications JB/T 8881-2011 5 |  |  |
|  |  | 4 | The depth of hardening layer | 030202 | Rolling bearings－Carburizing heat-treatment for parts－Specifications JB/T 8881-2011 5 | Except for:Macroscopic fracture method |  |
|  |  | 5 | Surfacecarbon | 020102 | Carbon and low-alloy steel-Determination of multi-element contents-Spark discharge atomic emission spectrometric method (routine method) GB/T 4336-2016 |  |  |
| 27 | Heat treated high carbon chromium stainless steel rolling bearing parts | 1 | The microstructure | 030204 | Rolling bearings－Bearing parts made from high-carbon chromium stainless steel －Specifications for heat-treatment JB/T 1460-2011 4 |  |  |
|  |  | 2 | Rockwell hardness | 030103 | Rolling bearings－Bearing parts made from high-carbon chromium stainless steel －Specifications for heat-treatment JB/T 1460-2011 4 | Accredited only for：HRC |  |
|  |  | 3 | Steel ball crushing load | 030199 | Rolling bearings－Bearing parts made from high-carbon chromium stainless steel －Specifications for heat-treatment JB/T 1460-2011 4 | Accredited only for：≤2000kN |  |
| 28 | Parts made from Cr4Mo4V bearing steel elevated temperature | 1 | The microstructure | 030204 | Rolling bearings—Parts made from Cr4Mo4V bearing steel elevated temperature—Specifications for heat-treatment JB/T 2850-2007 4 |  |  |
|  |  | 2 | Rockwell hardness | 030103 | Rolling bearings—Parts made from Cr4Mo4V bearing steel elevated temperature—Specifications for heat-treatment JB/T 2850-2007 4 | Accredited only for：HRC |  |
|  |  | 3 | Steel ball crushing load | 030199 | Rolling bearings—Parts made from Cr4Mo4V bearing steel elevated temperature—Specifications for heat-treatment JB/T 2850-2007 4 | Accredited only for：≤2000kN |  |
| 29 | Mechanical components (geometry) | 1 | circular degree | 030704 | Rolling bearings—Methods for the measurement and assessment of departure from roundness and waviness GB/T 32324-2015 4.1.3,6.1.1 |  |  |
|  |  |  |  |  | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.3 |  |  |
|  |  | 2 | roughness | 030704 | Rolling bearing parts-Methods for the measurement and assessment of surface roughness JB/T 7051-2006 5.1,5.2,5.3,5.4,6.1 |  |  |
|  |  | 3 | measurement | 030704 | Geometrical product specifications (GPS) - Inspection of plain workpiece sizes GB/T 3177-2009 |  |  |
|  |  | 4 | straightness | 030704 | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.1 |  |  |
|  |  | 5 | flatness | 030704 | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.2 |  |  |
|  |  | 6 | cylindricity | 030704 | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.4 |  |  |
|  |  | 7 | depth of parallelism | 030704 | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.7 |  |  |
|  |  | 8 | verticality | 030704 | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.8 |  |  |
|  |  | 9 | slope | 030704 | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.9 |  |  |
|  |  | 10 | concentricity | 030704 | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.10 |  |  |
|  |  | 11 | position accuracy | 030704 | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.12 |  |  |
|  |  | 12 | degree of symmetry | 030704 | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.11 |  |  |
|  |  | 13 | Circular Runout | 030704 | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.13 |  |  |
|  |  | 14 | total run-out | 030704 | Geometrical porduct Specifecations(GPS)--Geometrical tolerance--Verification prescription GB/T 1958-2004 appendixA A.6.14 |  |  |
| 30 | Metal materials and metal parts | 1 | Tensile experiment | 030101 | Metallic materials - Tensile testing - Part 1 : Method of test at room temperature GB/T 228.1-2010 7,8,10,11,12,13,20,21,22 | Accredited only for：≤600kN,Method B:Rm,A,Z,ReL,Rp |  |
|  |  | 2 | Impact test | 030104 | Metallic materials—Charpy pendulum impact test method GB/T 229-2007 8 | Accredited only for：Indoortemperature to - 40℃,≤300J,KV2 |  |
|  |  | 3 | Rockwell hardness | 030103 | Metallic materials - Rockwell hardness test - Part 1: Test method(scales A、B、C、D、E、F、G、H、K、N、T) GB/T 230.1-2009 7.9 | Accredited only for：HRC |  |
|  |  | 4 | Vickers hardness | 030103 | Metallic materials—Vickers hardness test—Part 1:Test method GB/T 4340.1-2009 7 | Accredited only for：HV1 |  |
|  |  | 5 | Brinell hardness | 030103 | Metallic materials—Brinell hardness test—Part 1:Test method GB/T231.1-2009 7 | Accredited only for：HBW10/3000,HBW10/1000,HBW5/75O,HBW5/250 |  |
|  |  | 6 | Grain size | 030201 | Metal-methods for estimating the average grain size GB/T 6394-2002 5.1 | Accredited only for：Comparison method |  |
|  |  | 7 | The microstructure | 030204 | Steel－Determination of microstructure GB/T 13299-1991 4.5 | Accredited only for：Free cementite and banded structure |  |
|  |  | 8 | Non-metallic inclusions | 030203 | Steel—Determination of content of nonmetallic inclusions—Micrographic method using standards diagrams GB/T 10561-2005 5.2.1 | Accredited only for：A method |  |
|  |  | 9 | The macrostructure | 030205 | Test method for macrostructure and defect of steel by etching GB/T 226-2015 4.2 | Accredited only for：Hot acid corrosion |  |
|  |  | 10 | The depth of decarburization layer | 030202 | Determination of depth of decarburization of steels GB/T 224-2008 4.2 | Accredited only for：Metallographic method |  |
|  |  |  |  |  | Rolling bearings--Determination of decarburized depth for parts JB/T7362-2007 4.1 |  |  |
|  |  | 11 | Carbide is not uniformity | 030204 | Eutectic carbide of steel－Micrographic method using standard diagrams GB/T 14979-1994 4.2,4.3,4.4,5 |  |  |
|  |  | 12 | C,S | 020108 | Steel and iron –Determination of total carbon and sulfur content Infrared absorption method after combustion in an induction furnace (routine method) GB/T 20123-2006 |  |  |
|  |  | 13 | C，S，Si，Ni，Mo,P,Cr,Mn, Cu,Al,As,Sn,Ti | 020102 | Carbon and low-alloy steel-Determination of multi-element contents-Spark discharge atomic emission spectrometric method (routine method) GB/T 4336-2016 |  |  |
|  |  | 14 | C，S，Si，Mn,P,Cr,Ni, Mo,Cu，Al,Ti | 020102 | Stainless steel-Determination of multi-element contents-Spark discharge atomic emission spectrometric method (Routine method) GB/T 11170-2008 |  |  |
|  |  | 15 | Ca | 020102 | Standard Test Method for Analysis of Carbon and Low-Alloy steel by Spark Atomic Emission Spectrometry ASTM E415-2015 |  |  |
|  |  | 16 | Si，Mn,P,Ni,Cr, Mo,Cu,Al,Ti | 020101 | Low-alloy steel-Determination of multi-element contents-inductively coupled plasma atomic emission spectrometric method GB/T20125-2006 |  |  |
|  |  | 17 | Si，Mn,P,Ni,Cr, Mo,Cu,Ti | 020101 | Determination of chemical composition in stainless steel-Inductively coupled plasma atomic emission spectrometric method SN/T2718-2010 |  |  |
|  |  | 18 | Si，Mn,P,Cr,Ni, Al,Pb,Sn | 020101 | Methods for chemical analysis of copper and copper alloys- part27: The inductively coupled plasma atomic emission spectromertric method GB/T 5121.27-2008 |  |  |
|  |  | 19 | Cu | 020114 | Determination of copper content for brass- iodimetry YS/T910-2013 |  |  |
|  |  | 20 | O | 020109 | Steel and iron-Determination of oxygen content-The pulse heating inert gas fusion-infra-red absorption method GB/T 11261-2006 |  |  |
|  |  | 21 | N | 020109 | Steel and iron-Determination of nitrogen content-Thermal conductimetric method after fusion in a current of inert gas (Routine method) GB/T 20124-2006 |  |  |
|  |  | 22 | Ultrasonic testing | 110202 | Steel forgings - Method for ultrasonic testing GB/T 6402-2008 |  |  |
|  |  |  |  |  | Forged and rolled steel bars -method for ultrasonic testing GB/T 4162-2008 |  |  |
|  |  | 23 | Magnetic particle testing | 110203 | Rolling bearings - Non-destructive testing - Magnetic particle testing GB/T 24606-2009 |  |  |
|  |  |  |  |  | Magnetic particle inspection method of rolling bearings for locomotive and rolling stock wheel sets TB/T 1987-2003 |  |  |
|  |  | 24 | Penetration testing | 110204 | Non-destructive Testing - Test Method for Penetrant Testing JB/T 9218-2015 |  |  |
| 31 | High carbon chromium stainless steels | 1 | Non-metallic inclusions | 030203 | High carbon chromium stainless bearing steels GB/T 3086-2008 7 | Accredited only for：A method |  |
|  |  | 2 | The microstructure | 030204 | High carbon chromium stainless bearing steels GB/T 3086-2008 7 |  |  |
|  |  | 3 | Uniformity of carbide | 030204 | High carbon chromium stainless bearing steels GB/T 3086-2008 7 |  |  |
|  |  | 4 | The depth of decarburization layer | 030202 | High carbon chromium stainless bearing steels GB/T 3086-2008 7 | Accredited only for：Metallographic method |  |
|  |  | 5 | The macrostructure | 030205 | High carbon chromium stainless bearing steels GB/T 3086-2008 7 | Accredited only for：Hot acid corrosion |  |
|  |  | 6 | C,S | 020108 | Steel and iron –Determination of total carbon and sulfur content Infrared absorption method after combustion in an induction furnace (routine method) GB/T 20123-2006 |  |  |
|  |  | 7 | P,Si,Cr,Mo, Mn,Ni,Cu | 020102 | Carbon and low-alloy steel-Determination of multi-element contents-Spark discharge atomic emission spectrometric method (routine method) GB/T 4336-2016 |  |  |
| 32 | carburizing steels of bearings | 1 | Grain size | 030201 | Specification for carburizing steels of bearings GB3203-82 3 | Accredited only for：Comparison method |  |
|  |  | 2 | The microstructure | 030204 | Specification for carburizing steels of bearings GB3203-82 3 |  |  |
|  |  | 3 | Non-metallic inclusions | 030203 | Specification for carburizing steels of bearings GB3203-82 3 | Accredited only for：A method |  |
|  |  | 4 | The macrostructure | 030205 | Specification for carburizing steels of bearings GB3203-82 3 | Accredited only for：Hot acid corrosion |  |
|  |  | 5 | Brinell hardness | 030103 | Specification for carburizing steels of bearings GB3203-82 3 | Accredited only for：HBW10/3000,HBW10/1000,HBW5/75O,HBW5/250 |  |
|  |  | 6 | C,S | 020108 | Steel and iron –Determination of total carbon and sulfur content Infrared absorption method after combustion in an induction furnace (routine method) GB/T 20123-2006 |  |  |
|  |  | 7 | Si,Mn,Cr,Ni,Mo,Cu,P | 020101 | Low-alloy steel-Determination of multi-element contents-inductively coupled plasma atomic emission spectrometric method GB/T20125-2006 |  |  |
|  |  | 8 | C，S，Si，Mn,Cr,Ni,Mo,Cu,P | 020102 | Carbon and low-alloy steel-Determination of multi-element contents-Spark discharge atomic emission spectrometric method (routine method) GB/T 4336-2016 |  |  |
| 33 | High-carbon chromium bearing steel | 1 | Non-metallic inclusions | 030203 | High-carbon chromium bearing steel GB/T 18254-2002 6.6 | Accredited only for：A method |  |
|  |  |  |  |  | High-carbon chromium bearing steel wires GB/T 18579-2001 6.6 |  |  |
|  |  | 2 | The microstructure | 030204 | High-carbon chromium bearing steel GB/T 18254-2002 6.7 |  |  |
|  |  |  |  |  | High-carbon chromium bearing steel wires GB/T 18579-2001 6.6 |  |  |
|  |  | 3 | Uniformity of carbide | 030204 | High-carbon chromium bearing steel GB/T 18254-2002 6.8 |  |  |
|  |  |  |  |  | High-carbon chromium bearing steel wires GB/T 18579-2001 7.8 |  |  |
|  |  | 4 | Microscopic pores | 030204 | High-carbon chromium bearing steel GB/T 18254-2002 6.9 |  |  |
|  |  |  |  |  | High-carbon chromium bearing steel wires GB/T 18579-2001 7.8 |  |  |
|  |  | 5 | The depth of decarburization layer | 030202 | High-carbon chromium bearing steel GB/T 18254-2002 6.5 | Accredited only for：Metallographic method |  |
|  |  |  |  |  | High-carbon chromium bearing steel wires GB/T 18579-2001 6.6 |  |  |
|  |  | 6 | The macrostructure | 030205 | High-carbon chromium bearing steel GB/T 18254-2002 6.4 | Accredited only for：Hot acid corrosion |  |
|  |  |  |  |  | High-carbon chromium bearing steel wires GB/T 18579-2001 7.8 |  |  |
|  |  | 7 | Brinell hardness | 030103 | High-carbon chromium bearing steel GB/T 18254-2002 6.11 | Accredited only for：HBW10/3000,HBW10/1000,HBW5/75O,HBW5/250 |  |
|  |  | 8 | Tensile experiment | 030101 | High-carbon chromium bearing steel wires GB/T 18579-2001 6.5 | Accredited only for：≤600kN,Method B:Rm,A,Z,ReL,Rp |  |
|  |  | 9 | C,S | 020108 | Steel and iron –Determination of total carbon and sulfur content Infrared absorption method after combustion in an induction furnace (routine method) GB/T 20123-2006 |  |  |
|  |  | 10 | C，S，P，Si，Cr,Mo,Mn,Ni,Cu | 020102 | Carbon and low-alloy steel-Determination of multi-element contents-Spark discharge atomic emission spectrometric method (routine method) GB/T 4336-2016 |  |  |
| 34 | Cold rolled steel sheets and strips | 1 | Tensile experiment | 030101 | Cold rolled quality carbon structural steel sheets and strips GB/T13237-2013 7 | Accredited only for：≤600kN,Method B:Rm,A,Z,ReL,Rp |  |
|  |  | 2 | Grain size | 030201 | Cold rolled quality carbon structural steel sheets and strips GB/T13237-2013 7 | Accredited only for：Comparison method |  |
|  |  | 3 | Free cementite | 030204 | Cold rolled quality carbon structural steel sheets and strips GB/T13237-2013 7 |  |  |
|  |  | 4 | C,S | 020108 | Steel and iron –Determination of total carbon and sulfur content Infrared absorption method after combustion in an induction furnace (routine method) GB/T 20123-2006 |  |  |
|  |  | 5 | Si,Mn,P,Cr, Ni,Cu,Al | 020101 | Low-alloy steel-Determination of multi-element contents-inductively coupled plasma atomic emission spectrometric method GB/T20125-2006 |  |  |
|  |  | 6 | C，S，Si,Mn,P,Cr, Ni,Cu,Al | 020102 | Carbon and low-alloy steel-Determination of multi-element contents-Spark discharge atomic emission spectrometric method (routine method) GB/T 4336-2016 |  |  |
| 35 | Hot-rolled plates sheets and wide strips | 1 | Tensile experiment | 030101 | Hot-rolled quality carbon structural steel plates 、sheets and wide strips GB/T711-2008 7 | Accredited only for：≤600kN,Method B:Rm,A,Z,ReL,Rp |  |
|  |  | 2 | C,S | 020108 | Steel and iron –Determination of total carbon and sulfur content Infrared absorption method after combustion in an induction furnace (routine method) GB/T 20123-2006 |  |  |
|  |  | 3 | Si,Mn,P,Cr, Ni,Cu | 020101 | Low-alloy steel-Determination of multi-element contents-inductively coupled plasma atomic emission spectrometric method GB/T20125-2006 |  |  |
|  |  | 4 | C，S，Si,Mn,P,Cr, Ni,Cu | 020102 | Carbon and low-alloy steel-Determination of multi-element contents-Spark discharge atomic emission spectrometric method (routine method) GB/T 4336-2016 |  |  |
| 36 | Extruded tube of copper and copper alloys | 1 | Tensile experiment | 030101 | Extruded tube of copper and copper alloys YS/T662-2007 4..3 | Accredited only for：≤600kN,Method B:Rm,A,Z,ReL,Rp |  |
|  |  | 2 | Brinell hardness | 030103 | Extruded tube of copper and copper alloys YS/T662-2007 4..3 | Accredited only for：HBW10/3000,HBW10/1000,HBW5/75O,HBW5/250 |  |
| 37 | alloy steel forgings | 1 | Tensile experiment | 030101 | Specification for the heavy alloy structural steel forgings JB/T6396-2006 5.2 | Accredited only for：≤600kN,Method B:Rm,A,Z,ReL,Rp |  |
|  |  | 2 | Impact test | 030104 | Specification for the heavy alloy structural steel forgings JB/T6396-2006 5.2 | Accredited only for：INdoortemperature to - 40℃,≤300J,KV2 |  |
| 38 | Lubricating grease | 1 | Dropping point | 021002 | Lubricating grease -Determination of dropping point GB/T4929-1985 |  |  |
|  |  | 2 | Cone penetration | 021002 | Lubricating grease and petrolatum -Determination of cone penetration GB/T269-1991 | Accredited only for Full scale cone method |  |
| 39 | Lubricating oil | 1 | Kinematic viscosity | 021003 | Petroleum products-Determination of kinematic viscosity and calculation of dynamic viscosity GB/T 265-1988 | 40℃、100℃ kinematic viscosity |  |
|  |  | 2 | Flash point | 021003 | Petroleum products-Determination of flash and fire points-Cleveland open cup method GB/T 3536-2008 |  |  |

组长/组员签字：

附表3-1                                                   任务编号：L21135-2016-01

推荐认可的实验室检测能力范围（中文）

名称：洛阳LYC轴承有限公司检测试验中心

地址：洛阳市洛龙区张衡街1号

| 序号 | 检测对象 | 项目/参数 | 领域代码 | 检测标准（方法）名称及编号（含年号） | 说明 | 备注 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | 序号 | 名称 |  |  |  |  |
| 1 | 机械零部件（几何尺寸） | 1 | 尺寸 | 030701 | 产品几何技术规范(GPS) 光滑工件尺寸的检验 GB/T 3177-2009 |  |  |
|  |  | 2 | 直线度 | 030701 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.1 |  |  |
|  |  | 3 | 平面度 | 030701 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.2 |  |  |
|  |  | 4 | 圆度 | 030701 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.3 |  |  |
|  |  | 5 | 圆柱度 | 030701 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.4 |  |  |
|  |  | 6 | 平行度 | 030701 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.7 |  |  |
|  |  | 7 | 垂直度 | 030701 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.8 |  |  |
|  |  | 8 | 倾斜度 | 030701 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.9 |  |  |
|  |  | 9 | 同轴度 | 030701 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.10 |  |  |
|  |  | 10 | 位置度 | 030701 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.12 |  |  |
|  |  | 11 | 对称度 | 030701 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.11 |  |  |
|  |  | 12 | 圆跳动 | 030701 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.13 |  |  |
|  |  | 13 | 全跳动 | 030701 | 产品几何量技术规范 (GPS) 形状和位置公差检测规定 GB/T 1958-2004 附录A A.6.14 |  |  |
| 2 | 滚动轴承 | 1 | 密封性能 | 030704 | 滚动轴承 密封深沟球轴承 防尘、漏脂及温升性能试验规程 GB/T 32321-2015 | 只测：12mm≤d≤60mm |  |
|  |  | 2 | 寿命试验 | 030704 | 滚动轴承 寿命与可靠性试验及评定 GB/T 24607-2009 |  |  |
|  |  |  |  |  | 滚动轴承 汽车轮毂轴承单元 JB/T 10238-2011 | 只测：30mm≤d≤100mm |  |

组长/组员签字：

附表3-1                                                 任务编号：L21135-2016-01

推荐认可的实验室检测能力范围（英文）

Lab：Test Center of Luoyang LYC Bearing Co., Ltd.

Add：No.1 Zhangheng Road,Luolong Diserict,Luoyang City.China

| №. | Test object | Item/ Parameter | Code of field | Title， Code of standard or method | Note | Expansion or change |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | №. | Item/ Parameter |  |  |  |  |
| 1 | General components and parts | 1 | demention | 030701 | Geometrical Product Specifications(GPS)-Inspection of plain workpiece sizes GB/T 3177-2009 |  |  |
|  |  | 2 | straightness | 030701 | Geometrical product Specifications(GPS)-Geometrical tolerance-Verification prescription GB/T 1958-2004 appendix A A.6.1 |  |  |
|  |  | 3 | planeness | 030701 | Geometrical product Specifications(GPS)-Geometrical tolerance-Verification prescription GB/T 1958-2004 appendix A A.6.2 |  |  |
|  |  | 4 | roundness | 030701 | Geometrical product Specifications(GPS)-Geometrical tolerance-Verification prescription GB/T 1958-2004 appendix A A.6.3 |  |  |
|  |  | 5 | cylindrictiy | 030701 | Geometrical product Specifications(GPS)-Geometrical tolerance-Verification prescription GB/T 1958-2004 appendix A A.6.4 |  |  |
|  |  | 6 | parallelism | 030701 | Geometrical product Specifications(GPS)-Geometrical tolerance-Verification prescription GB/T 1958-2004 appendix A A.6.7 |  |  |
|  |  | 7 | perpendicularity | 030701 | Geometrical product Specifications(GPS)-Geometrical tolerance-Verification prescription GB/T 1958-2004 appendix A A.6.8 |  |  |
|  |  | 8 | angularity | 030701 | Geometrical product Specifications(GPS)-Geometrical tolerance-Verification prescription GB/T 1958-2004 appendix A A.6.9 |  |  |
|  |  | 9 | concentricity | 030701 | Geometrical product Specifications(GPS)-Geometrical tolerance-Verification prescription GB/T 1958-2004 appendix A A.6.10 |  |  |
|  |  | 10 | position | 030701 | Geometrical product Specifications(GPS)-Geometrical tolerance-Verification prescription GB/T 1958-2004 appendix A A.6.12 |  |  |
|  |  | 11 | symmetry | 030701 | Geometrical product Specifications(GPS)-Geometrical tolerance-Verification prescription GB/T 1958-2004 appendix A A.6.11 |  |  |
|  |  | 12 | circular runout | 030701 | Geometrical product Specifications(GPS)-Geometrical tolerance-Verification prescription GB/T 1958-2004 appendix A A.6.13 |  |  |
|  |  | 13 | total runout | 030701 | Geometrical product Specifications(GPS)-Geometrical tolerance-Verification prescription GB/T 1958-2004 appendix A A.6.14 |  |  |
| 2 | Rolling Bearing | 1 | Sealing Property | 030704 | Rolling bearings—Sealed deep groove ball bearings—Performance test rule of dustproofing,grease leakage and temperature rise GB/T 32321-2015 | Accredited only for:12mm≤d≤60mm |  |
|  |  | 2 | Life Test | 030704 | Test and evaluation of life and reliability of rolling bearing GB/T 24607-2009 |  |  |
|  |  |  |  |  | Rolling bearing automobile wheel hub bearing unit JB/T 10238-2011 | Accredited only for:30mm≤d≤100mm |  |

组长/组员签字：